BUZZ MODELS

‘O’ Gauge Specialists

68 Meadow Road

Kingswood

Garston

WD25 0JA

E-mail: buzzmodels@gmail.com

FNA Flask wagon

This kit covers 550015 to 550060

Can cover 550009 to 550014 in modified form

First of all thank you for buying this kit, and good luck. It was designed to be a representation of the wagon not a spot on kit. It is recommended that you get plenty of photo’s of your chosen prototype.

To complete you will need glue, solder, paint, transfers and wheels.

We recommend Slater’s wheels Ref.7122D, but other ones are available.

Transfers for the FNA are available from Fox Transfers ref. F7190, or Railtec Transfers ref. 7282

List of Parts

1 piece Frame. 1 piece Hood. 2 Hood Catches (handed).

2 Bogie Kits. 4 Buffers. 2 Hood Wheels. 2 End Handrails. Brass wire.

2x 6BA Counter sink bolt and Nuts. 2 Lamp brackets, 2 Brake pipes.

Please refer to photo page whilst building.

General Notes

To save repeating instruction that applies to all sections.

1/ Identify all parts

2/ Wash all resin parts in warn soapy water to remove the releasing agent.

3/ Clean flash and mould lines from the castings. Be careful not to remove too much of the castings. On newer Frame casting you may need to flatten the sides. Be careful not to remove the raised details

Frame

1/ Drill out holes for buffer and fit.

For couplings you will need to mark the centre line

and drill a slot for coupling to fit into. Fit Lamp Bracket

Brake Pipe and couplings as per photo.

2/ Bogie pivot:- Remove the moulded bogie pivot Down to the square base (this was for the original design bogie) On new mouldings this has been done for you.  On the square base mark and drill at the centre, all the way through the Frame. From top counter-sink the hole and fit bolt. Cover with filler and rub smooth.

Bogie Pivot Before and After

3/  Measure in 72mm from buffer beam and down 6mm at

end without container stand, and drill hole and fit hood

wheel. (see photo)

4/  End Handrails. On older mouldings, the outer 2 marks are in the wrong place. From the centre mark measure out 19mm and drill new hole, in-line with old marks. You might wish to replace the casting with stronger wire(not supplied). Fit Handrail with triangle bits inwards.

Hood

5/  Drill and fit small piece of wire into the hole on both

sides at the platform end to form the hood catch points.

6/ Fit Hood to Frame then fit Hood catches, with hooks over the small bits of wire fitter in 5.  A length of wire now connects the 2 catches together.

Bogies

7/   Drill out the axle boxes to clear your choice of bearings, and fit. Place wheels into bearings then attach sides to bogie bolster.

8/ Attach end stretchers, then attach handbrake wheels.

Note 2 different type of stretcher, the ones with indicator

plates go at the handbrake-outer end. (see photo)

Livery

These wagons were built in stainless steel and were left unpainted, except buffers and bogies which are black and the flask hood which is rail white. Over the years the body has weathered to a brown colour.

Further Reading

More information can be found in these publications.

Working Wagons Vol4 1985-1992 by David Larking  ISBN 0-9538448-4-6

British Railway Goods Wagons in Colour 1960-2003 by Robert Hendry  ISBN 1-85780-170-9

Model Rail No 51 January 2003 and No 52 February 2003

© Buzz Models & MTH 2022